## Slide 1: 6 JAN : INTRODUCTION TO C BASED VLSI DESIGN
Very Large Scale Integration
Allows thousand of electronic components to be placed on single chip
VLSI affords IC designers the ability to design utilizing less space.
How to transform C- Code into its corresponding hardware , how to design c code for effective system generation and how to enhance circuit efficiency
Can we do this task automatic ? Using any rule
HLS
STEPS
DRAW DIFF GRAPH AND UNDERSTAND DEPENDENCY
CONTROL AND DATA FLOW
SPLIT OP INTO 3 ADDR FORMAT
DATA DEPENCEY

## Slide 2: 9 JAN : C TO RTL WITH EXAMPLES
CHIP : DIRECTLY WITH RESOURCES WASTE
ANY POSSIBLE WAY FOR OPTIMIZED
AUTOMATION METHOD:
1ST : DRAW DIFFERENTIAL GRAPH
UNDERSTAND DEPENDENCIES
2nd : Control and Data flow
3rd : DATA DEPENDENCY
CONTROL AND DATA FLOW GRAPH
DIFFERENTIAL EQUATION WALA EXAMPLE

## Slide 3: 13 JAN : HLS STEPS : HIGH LEVEL SYNTHESIS
1 . HLS : It is a process that generates efficient hardware at RTL from high-level code
May or may not generate the most efficient hardware at RTL
Depends on efficiency : which type u want
Fastest or with minimum resources or at equivalence
STEPS :
1> PREPROCESSING : CONTROL FLOW AND DATA FLOW GRAPH
HOW U KNOW DATA DEPENDENCY ? USING THIS GRAPH
2> SCHEDULING : DECIDE NO OF CLOCKS AND OPERATIONS IN EACH CLOCK
WHICH OPTIMIZATION U WANT ?
BOTH EQUALIZE
MINM TIME OR MINIM RESOURCES
3> ALLOCATION AND BINDING :
REG & FUNC UNIT : NOW ALLOCATE AND BIND
4> DATA PATH GENERATION
5> CONTROLLER GENERATION
WE BREAK DOWN INTO 3 ADDRESS FORMAT

## Slide 4: 16 JAN : VERILOG

## Slide 5: 17 JAN : VIVADO TOOL

## Slide 6: 23 JAN : FUNCTIONAL PIPELINING IN HLS
SPECIFY PIPELINE : IT WILL PIPELINE YOUR HLS
EX : #pragma HLS function pipeline II (<int>)
#pragma HLS pipeline II = 2
Specify it : it will design by itself,
Initiation interval : means the time after which we provide another input
LATENCY : THE TIME IT TAKE TO EXECUTE A INPUT
THROUGHPUT : HOW OFTEN WE GET OUTPUT
II = 1 : FULLY PIPELINED
IF U DIDN’T MENTION II = <int> , BY DEFAULT II = 1
NOTE GIVEN A DESIGN LATENCY CAN’T BE CHANGE
WE CAN ONLY CHANGE THROUGHPUT / INITIATION INTERVAL

## Slide 7: 24 JAN : LOOP PIPELINE IN HLS
II : INITIATION INTERVAL : NO OF CYCLES B/W STARTING OF TWO ITERATIONS
LATENCY : NO OF CYCLES NEEDED TO PROCESS ONE SET OF INPUTS
THROUGHPUT : NO OF CYCLES
LOOP :
PIPELINE
UNROLLED / UNROLLED WITH RESOURCE CONSTRAINTS : ARRAY MAPPED TO REG : SO STATIC SIZE OF ARR
PARTIAL UNROLLING
Performance is coming with cost of resources so we prefer less resources also
NOTE : IF THERE IS DATA DEPENDENCY WE CAN’T DO UNROL DIRECTLY
#pragma HLS unroll factor=<N>
The factor specifies how many times to unroll the loop. If it is not specified, or specified as N
NOTE UNROLL FACTOR = 8, 10
ETC
IN THIS CASE DUAL PORT CANNOT IMPROVE THE PERFORMANCE.
SO WE DO PARTITIONING OF ARRAY
IF DIFF BLOCKS WE CAN ACCESS RAM
BASED ON ACCESS PATTERN
BLINDLY UNROLLING MAY NOT HELP
PARTIAL UNROLL -> PARTITION THE ARRAY BASED ON ACCESS